## Slide 1: Hilti Simulation Platform

## Slide 2: Agenda
Idea
1
HW Architecture
2.1
Initial Position
1.1
Basic Idea
1.2
Archtiecture/Features
2
Development Environment
2.2
SW-Architechture
2.3
Live Demo
Actual Status
3
2.4

## Slide 3: Initial Position
Currently the development support concerning test- and simulation- utilities is almost zero. Each project spends a non negligible effort to develop utilities to test the target SW during the development phase.
There are some small proprietary non coupled tools to provide simple utilities like UART communication or HALL generation.
All the utilities need an own eval board, there is no possility to coordinate the actions.
Hard to reproduce and to maintain

## Slide 4: Basic Idea
Provide a simple simulation platform for all typical JDS projects to reduce development effort and increase SW quality by continuously developing stimuli scenarios beside the appropriate target SW.
Test Utilities/Components should be reusable accross projects and teststages to further reduce effort.
The usage of the simulation platform should be as simple as possible.

## Slide 5: HW-Architecture
The basic HW-Architecture is to connect two Evalboards on the uC-Pin level. One Eval Board to provide all necessaries signals to stimulate the target SW.
Simulationplatform NUCLEO-144F7xx
(STM32 Cortex M7)
Target SW running on Eval XY
(no instrumentation)
Connection Matrix (possibility to connect SALEA/Oszi/Multimeter)
analog
digital IOs
PWM
HALL-Gen
Power supply
Signal conditioning
Debug output
Manual control/debug
SPI/I2C/
UART

## Slide 6: HW-Architecture (detailed features)
Power Supply 5V 1A / 3,3V 500mA
Optional Supply 40V
Up to 18 analog outpts (0..3,3V, 2*internal DAC; 16*external DAC)
2*SPI / 2*I2c / 2*UART
10 Digital I/Os
8*OPV Channels for analog signal conditioning
4*3,3V=>5V level shifter for UART adaption
4*5v=>3,3V level shifter
4* level shifter up 40V (controlled via analog output)
1* 3 phase PWM input to measure PWM Duty
1* 3 phase HALL generation
1* dedicated UART for Akku communication
4* poti for manual testing
4* switch for manual testing
4* Jumper for manual testing
4* LED status output

## Slide 7: Development Environment (simulator development)
To provide a high level SW interface the modeling tool eTrice will be used to generate the simulation code.
For driver development the Cube Tool is used to minimize simulation development effort.
eTrice
Cube
Manual Code
ST-Libraries
GNU Compiler/Linker
ST-Link2 Debugger
C-Code Gen
C-Code Gen
Eclipse CDT + ST-Device Support + eTrice Plugin

## Slide 8: SW-Architecture (simulator usage)
To make access as easy as possible a basic SW layer will be provided.
SW-Component representing the
simulation HW platform
Port with associates Protocol
to provide high level access to the HW functionality
User responsibility

## Slide 9: SW-Architecture (simulator usage)
To make access as easy as possible a basic SW layer will be provided.
User Testscenario
Additional reusable components

## Slide 10: SW-Architecture (simulator usage)
SW-Components can be designed as hierarchical FSM e.g. Motor-Simulation:

## Slide 11: Demo
www.eclipse.org/etrice
DEMO

## Slide 12: Actual Status (29.01.2017)
Two hand mande boards and two layouted boards available (Dgate small, SF6, SF4)
Allready supported tasks:
  Support for SF6 performance measurement
  SW verifcation for SF6 EOL-Test commands (simulation of testadapter)
  Bugreport verification (SF6 overcurrent detection)
  Akku simulation for Dgate testing under development.
  Automated DGate SW Verification (stand alone Version)
  Semi Automated DGate SW Verification (ODA-Version)
  SF4 Support for porting SF6 code to SF4 Cortex M0
Basic platform SW available
  NUCLEO F767 basic drivers
  PWM Duty measurement
  HALL generation variable speed
  Simple Motorsimulation (PWM Duty * X => HAL speed)
  Akku simulation for Dgate testing
  Simulation of Testadapter
  Poti Switch

## Slide 13: eTrice
Hilti Simulation Platform powered by eTrice.
www.eclipse.org/etrice

## Slide 14
Thank you

## Slide 15: SW-Architecture (simulator usage)
To make access as easy as possible a basic SW layer will be provided.
SW-Component representing the simulation HW platform
Port with associates Protocol
to provide high level access to the HW functionality
User responsibility
User Testscenario
Additional reusable components